## Slide 1: Summary
Customer sets VM’s latency sensitivity to “high” which has two effects
  Disable NIC interrupt coalescing.
  Gives the VCPUs exclusive affinity.
    A VCPU has exclusive ownership of PCPU
    Reduces average latency and jitter.

## Slide 2: Average latency
When a VCPU has exclusive affinity it can halt in the monitor rather than descheduling to the vmkernel when the guest halts.
  The PCPU wouldn’t be used for any other work
  Avoids scheduler and vmkcall overheads when unhalting.
  Retains power savings
APIC virtualization
PCI passthru interrupt hints and physical affinity.

## Slide 3: Guest configuration for jitter
Using Linux CPU sets allows a non-realtime kernel to provide nice jitter behavior.
  isolcpu kernel command line option keeps kernel tasks off of the chosen set of cpus.
    Retain some cpus for services and non-latency sensitive work.
  cset is used to run the latency sensitive workload on the isolated cpus.
  As a result we don’t need to focus on reducing jitter from management tasks (and VMware Tools).

## Slide 4: Guest configuration for average latency
nohz=off kernel command line option for RHEL6 avoids stopping the APIC timer on halt and restarting APIC timer on unhalt.
Using x2apic should be cheaper (but adds complication of vtd).

## Slide 5: Jitter
Move vmkernel timers off of PCPUs with exclusive affinity.
  Periodic timers that don’t need affinity need to be moved into system worlds.
Turn off busmem services
  Or make them do work in smaller batches.
For system worlds that need affinity, change them to do work in smaller batches.
  Currently only vmkernel PageCache identified.
With workarounds for these 3 issues cyclictest ran for 40 hours with only 3 samples above 25us (average latency was ~10us).

## Slide 6: Jitter 2
Prevent SMIs from occurring on host.
  Can check for SMIs by looking in /reliability/SMI/PCPUList/* in VSI.
  At the mercy of the BIOS
    Disabling things like USB, iLO, etc can help, but no guarantees. HP has a guide for what to disable.
Disable power management

## Slide 7: Measuring average Latency
https://wiki.eng.vmware.com/LowLatency/PingPongMeasurement
Keep a buffer of timestamp/name pairs.
Call out to vprobes at end of trace.
  Throttling this callout in C code to 1/10 reduces Vprobes cache pollution.
Can record times in to PRDA before target vcpu is known.
  Start at physical NIC interrupt and trace through vmkernel until action post to vcpu.
Last I did this there was still some unknown thing in the system that caused the average latency to change by several microseconds (in a bi or tri modal fashion) on the order of every 10 minutes, which made it hard to show benefit from small changes.

## Slide 8: Opportunities
Vmkcall
  Avoid touching DEBUG_CTL
Priv_HaltPauseLoop
  Move more out of the loop (eg TimeTracker_Halt).
BusMem_Sample
Posted interrupts
  Raise vmxnet3 interrupts from vmkernel.