## Slide 1: 128 VCPUs Revisited
Fred Jacobs, Monitor team, December 10th, 2013

## Slide 2: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 3: Goals
Maintain common case (few VCPUs): fast, small
Correctness when using 128 VCPUs
Reasonable performance for 128 VCPUs
Simplicity, maintainability: One monitor for all VCPU counts
Notes: correctness, simplicity, readability, comprehensibility, maintainability
Space, time costs:
Minimal, common, maximal across axes: VCPU, memory, etc
Workloads
Hardware
Hosted vs ESX

## Slide 4: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 5: Changes - Overview
VCPUSets
  DT, TimeTracker, SVGA, TC, CrossCalls, PhysMem, patchset, interrupts, monitor actions, VHV, VCPU Hotplug, checkpoint, monitor loop/pausing
  Constants for optimization
  Vmkernel: CpuSched remote requests
Variably-sized structures:
  VNPTShadowEntry, BusMemFrameSWMMU._mmuTraces
Switch paths: VMKCall, BackToHost
Firmware: SMRAM/SMM initialization (BIOS, EFI)
Guest OS: HV#2
Resource bumps:
  RPCConnections, max threads, max locks, world heap
vMotion: VCPU progress vs page-dirty backpressure (PR 1006716)
Notes: RPCConnections
VTHREAD_MAX_THREADS / cartelMaxThreads
MX_MAX_LOCKS
world heap size – WorldGroupNormalUseDelta – “Additional world group heap space” => federate, lock down

## Slide 6: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 7: Space Cost: Scopes
SMRAM (guest PA space)
vmm
vmx
vmkernel

## Slide 8: Space Cost: SMRAM
SMRAM (unique per-VCPU):
  SMBASE: Base address (PA)
  SMBASE+0x8000 -> SMBASE+0x81FF: SMI handler code
  SMBASE+0xFE00 -> SMBASE+0xFFFF: SMM save state
SMBASE set by chipset/firmware(/vmm)
SMRAM across VCPUs is interleaved
Traditional: ‘behind’ VGA RAM (0xA0000-0xBFFFF)
128 requires more
No more ‘behind’ memory available…
SMRAM device-backed, HWv11

## Slide 9: Space Cost: SMRAM vs Physical Memory
Notes: A picture of PA space layout, like what was on the whiteboard

## Slide 10: Space Cost: vmm
text, data, rodata static (MAX_VCPUS/NumVCPUs())
  dynamic: VNPTShadowEntry, BusMemFrameSWMMU._mmuTraces
sharedArea growth:
  SHARED_INTER_VCPU: 1 page/VCPU
  SHARED_INTER_VCPU_VMX: 2 pages/VCPU
  Net growth >= 768k
‘MONITOR’ VA space contended (0xFFFFFFFFFC000000-)
Notes: Text/data/rodata cannot be measured perfectly because so many other things changed simultaneously…

## Slide 11: Space Cost: vmm VA
“MONITOR” Virtual Address space, in 2MB pages (64MB at top)

## Slide 12: Space Cost: vmx
text, data, rodata static (MAX_VCPUS/NumVCPUs())
  Semaphores
  Locks (MX_MAX_LOCK)
  RPCConnections
  VTHREAD_MAX_THREADS, thread overhead

## Slide 13: Space Cost: vmkernel
text, data, rodata static (MAX_VCPUS/NumVCPUs())
  more worlds * more per-world costs
  World heap
  RPCConnections

## Slide 14: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 15: Open Issues
vmm cores
  !sparse, !deduped, scales with NumVCPUs()
  23GB vmmcores…
vmss2core + devSmram (PR 1066812)
coresPerSocket / vNUMA
  Windows socket limit
  vNUMA performance
  arch limits
SMRAM bring-up space waste/violates spec (PR 1054767)
  violates spec re SMBASE
  VGA_WINDOW vs device-backed
Notes: Arch limits: CPUID can only encode in 6 bits for some things, so no more than 64 cores per package
‘Free’ memory for suspend in legacy
mainMem behind VGA window pshared to zero for device-backed, so no notable net cost increase

## Slide 16: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 17: Performance
Crosscall scaling?
Scaling vs Gphys lock
MMUInfo 2MB
  ScratchAS for the shared area?
vNUMA/coresPerSocket (PR 1097867)
SAP HANA…

## Slide 18: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 19: Future Work: 129+ VCPUs
APIC vs X2APIC for numbering (“must” / “must not”)
VA space contention increases
Worse resources scaling (structure size ceilings)
  RPCConnections, …
Switch paths
  maximum args insufficient for yet bigger VCPUSets
… and things found empirically trying for 1024…
Notes: 8 args max on VMK IIRC… uglier for hosted.

## Slide 20: Future work: Trying for 1024 VCPUs
Extcfg doesn’t represent > 256 in a set
  Ditto VCPUNUMADeviceRead
VMSafe bits
vmkernel stack blown out by huge structs
mxState too big for the linker
Overhead memory
MAX_VCPUS vs print specifier
vmm VA space (128MB)
RPC blocks too large for monitor stack
More RPC blocks…
Interrupts/APIC IDs
SMRAM: VGA_WINDOW=>1MB fits 945 VCPUs
Notes: Vmkernel strict stack limits bumped

## Slide 21: Agenda
Goals
Changes
Space costs
Open issues
Performance
Future work
Stumbling blocks

## Slide 22: Stumbling Blocks
NUMA rebalance/initialization bugs
Weirdnesses re vmkernel heap sizing
VA space limits
Our PA space has no good map
Our VA space has a broken incomplete map
SMRAM users in firmware are confusing
  Dead code
  Live code which could be rewritten
  I may have found a legitimate use for non-BIOS SMM...