## Slide 1: MMU Virtualization
Raviprasad Mummidi

## Slide 2: Agenda
Address Translation in x86
Virtualized MMU
Non-Caching and Caching MMU
HV with Software MMU
HV with Hardware MMU

## Slide 3: Address Translation in x86
mov 0x1234, %eax
Virtual Address
(VA)
Linear Address
(LA)
Physical Address
(PA)
Bus Address
(BA)
Segmentation
Memory Management Unit
Chipset
Notes: 0x1234 is the virtual address.
Apply segmentation and the resulting address is called the linear address.
The linear address is the input to the MMU, which uses page tables to resolve the linear address to a physical address.
Hardware TLB gets populated with a mapping of LA->PA
Physical address is sent to the chipset and gets converted to a bus address depending on who own the physical address.

## Slide 4: x86 MMU
Hierarchical page-table data structure walked by hardware.
Hardware managed TLB caches results of page table walks.
Software required to follow semantics to invalidate TLB entry explicitly on mapping changes.
Software allowed to invalidate a single entry (INVLPG) or the whole TLB (CR3 reload/change, CR4 PGE flip) etc.
CR3 points to the page root. Can support 4, 3 or 2 level page table hierarchies.
Supports 4K, 2M or 4M, 1G sized physical pages.
Page table entries (PTEs) are of the form (page number + flags), where flags can be P, RW, U/S, NX etc.
Notes: Processors can have other internal caches which may be implementation specific.
Present to Non-Present or Present to Present needs explicit TLB invalidation. Not required to invalidate TLB on Non-Present to Present transitions.

## Slide 5: x86 MMU (contd.)
Example two level page table.
5
CR3
Directory Entry
Page Table
Page Table Entry
12
10
10
Physical Address
Directory
Table
Offset
PDE = Page Directory Entry
PTE = Page Table Entry
pde
pte
Data
Linear Address (32-bits)
Root

## Slide 6: Address Translation in x86 (virtualized view)
mov 0x1234, %eax
Hardware cannot walk guest page tables. It does not know that PPNs exist.
Virtual Address
(VA)
Linear Address
(LA)
Physical Address
(PA)
Bus Address
(BA)
DT
MMU
PhysMem
Machine Address
(MA)
BusMem
Notes: DT module virtualizes x86 segmentation and resolves VA to LA.
LA is translated to PA (guest physical address) by the MMU module.
MMU module walks the guest page table to resolve the LA to PA. Note that PA cannot be directly consumed by hardware. It is just another layer of indirection.
PA is converted to BA (bus address) with help from PhysMem module.
BA is resolved to MA with help from BusMem module. MA is the actual hardware address which the physical processor and chipset can understand.
A mapping from LA to MA is populated in what is called a shadow page table which is walked by the hardware.
As a result of the hardware page walk, hardware TLB gets populated with a mapping of LA to MA.

## Slide 7: Virtualized MMU
Virtual CR3 (VCR3)
pde
pte
Data
{ppn)
Page Table
{ppn)
Root
(ppn)
hardware CR3
pde
pte
MPN of Data
(mpn)
Shadow Page Table
(mpn)
Shadow Root
(mpn)
Guest View
Hardware View
Notes: MPNs for shadow root and shadow page table are allocated from the anonymous memory pool and is one of the important costs of doing MMU virtualization in s/w.
MPN for the DATA is its backing store.

## Slide 8: Hidden Page Fault
511 (Monitor)
  Hidden #PF => translation is present in the virtual page tree, but not in the shadow

## Slide 9: Hidden #PF (2)
The hardware IDTR always points at the monitor’s IDT.
So, on any #PF, monitor #PF handler is executed.
CR2 contains the linear address of the address which caused the fault.
After some house keeping, handler calls in to the MMU.
The page walker looks up guest page table while also validating the access.
Handler creates / updates shadow page table
  MPN (derived from PPN->MPN mapping)
  Permissions (either same or less permissive than the guest paging entry).
Handler resumes execution of the faulting guest instruction if the access was legal.
Notes: This is called a hidden #PF because the guest never sees these and it would not happen outside of virtualization.

## Slide 10: Hidden #PF (3)
511 (Monitor)

## Slide 11: Non-Caching MMU
First, also the simplest MMU implementation.
Shadow page tables populated lazily i.e. on guest access (when taking hidden #PFs).
Shadow page tables treated and managed as a large TLB.
Shadow page tables destroyed on guest CR3 reload or INVLPG.
Why ?
Cost of hidden #PF is high (several 1000s of cycles, vs. several 10s in hardware).
Notes: One address space can change paging entries that are used in another address space.

## Slide 12: Caching MMU
Reduce hidden #PFs by caching shadow mappings across CR3 changes.
Comes at a cost of having to keep shadow mappings coherent.
Shadow page tables need to be kept coherent with the guest page tables at all times.
MMU relies on physical traces to keep the shadow mappings up to date.
Notes: Hence need to get notified whenever the guest page table or root gets modified.
Caching MMU reduces the amount of work needed to done by the MMU on guest CR3 changes and after the CR3 change as well.

## Slide 13: Coherency using traces
Guest CR3 is mapped by PDE #1 at “LPN” in its address space as read/write (RW).
When mapping backing store mpn of VCR3(PPN1), permission of the shadow mapping is reduced to read-only (P) as the guest root is traced by the MMU.
When guest uses LPN to change PDE #3 to NP, a #PF is generated by hardware, as the shadow PTE is less permissive than that is required for the write to go through.

## Slide 14: Coherency (2)
Monitor #PF handler is executed
  Handler calls MMU, which checks guest permissions for LPN, write allowed. However, PPN1 has a MMU physical trace and so shadow mapping #1 is not updated and returns to the handler.
  PPN1 has MMU trace, so just restarting the instruction is not going to help make forward progress.
  Hence the guest instruction is single stepped using the x86 interpreter, which uses a writeable mapping of the guest CR3 in the monitor and notifies the MMU of the write.
Notes: MMU uses both write traces. In BT only after-write traces are used. However, in HV, before traces are used as well.

## Slide 15: Challenges ...
Guest modifies page tables a lot because what used to be a page table could now be a data page.
Shadow cache needs to be managed and needs to grow or shrink with guest working set and host overhead memory constraints.
Remote shadow page tables need to be updated when the primary page tables change.
  In a SMP guest, one VCPU might change another VCPU’s page table.
  Process migrations in the guest could leave shadow page tables behind on the VCPU where the process migrated from.
Notes: MMU uses many heuristics to determine when to drop the trace on the guest page table. If the heuristic is wrong, we might end up with a lot of #PFs.

## Slide 16: What makes Software MMU complicated ?
Monitor and guest share address space.
Various paging modes and different PTE formats, emulate permissions etc.
Rest of the Monitor relies on MMU to implement trace protection.
BT dependent TLBs.
Fast access to traced memory using MonTLB.
BT of guest CPL3 code @ hw CPL3.
BT relies on MMU to provide consistent LPN->BPN mapping with back to back page walks when performed during a virtual instruction execution and shield BT from inconsistencies that could arise due to other VCPU modifying the LPN->PPN mapping.

## Slide 17: Coping with guest paging modes
Irrespective of the guest paging mode, the page tree walked by hardware is always 4 levels as VMM is only 64bit.
When the platform bootstraps the monitor, it builds a set of page tables which together are called the “Cloud”.
The L4 page table built for the monitor by platform forms what we call as the non-caching/non-paging root. Never gets recycled and is called default root.
Non-caching/non-paging root is used when guest is in non-paging mode and also when using the non-caching MMU or when guest root tracing is disabled.
When guest is in non-paging mode, there is no VCR3 or page tree and hence shadow page tables emulate physical hardware behavior by having identical mappings from LPNs i.e. LPN = PPN.
Notes: When using HV, the platform root becomes the scratch AS root. The metadata for default root is stored in shadow cache entry 0, which never gets recycled.

## Slide 18: Guest paging modes (2)
When guest paging mode is less than 4 levels, the missing levels required by hardware are emulated with (flat) shadow page tables.
Example: Guest using a 2 level page table
Root
Page table
Emulated L4
Emulated L3
Shadow L2
Shadow L1
Monitor
Notes: Also when emulating large pages on platforms that do not support large pages, FLAT shadows are used.

## Slide 19: Guest Paging Modes (3)
Shadow L2
Monitor
Monitor
Monitor and guest sharing the address space.
Shadow L3
Shadow L4
Guest
Guest
Guest
Guest
Monitor
Monitor
Guest
511
511
479
…
…
511
0
…
…
…
510
0
…
…
…
510
Notes: When guest overlaps with the monitor “cloud” address space (last L4E tree in 4-level paging mode), monitor gets mapped in to the shadow page tables corresponding to the guest page table tree.

## Slide 20: Guest Paging Modes (4)
Handling 32-bit and 64-bit guest PTE types
Virtualizing guest U/S, G, NX bits
Handling guest accesses to top 64M of address space where monitor is mapped.
Guest large pages (2M, 4M, 1G).
Notes: When emulating 32-bit PTEs, each guest page table is shadowed by 2 MPNs instead of using just one MPN which is the case when shadow PTE size matches the guest PTE size.
Guest instructions accessing top 64M of address space are either passed through using a hole in the monitor address space or are simulated/interpreted.

## Slide 21: MMU’s role in traces
MMU is tasked with implementing the page protection essential for traces to be functional and effective.
Reducing permissions for traces can be done in two ways.
  Change/remove all shadow PTEs or
  Change shadow PTEs corresponding to a particular BPN of interest.
First one is easy and is implemented by MMU_ZapAll.
Frequent use of traces by Code tracing, page table traces, page sharing, ballooning, devices etc. Cannot get away with killing all the shadow PTEs all the time.
Access masking of specific shadow PTEs mapping a particular BPN/MPN is hard without spending more overhead memory to store back pointer.
MMU uses mtags.
Notes: There is no direct correlation between shadow PTE offsets and the guest physical addresses.
Mtag is a back pointer. In MMU it is used as a back pointer from BPN/MPN to the shadow PTE offset (shadow cache index + offset)

## Slide 22: MMU overheads
MPNs to back shadow page table / root MPNs (Shadow cache objects).
Metadata for shadow cache objects.
Given a page table BPN, need to quickly get to its shadow cache object. (Shadow cache list head)
Given a BPN need to get to all the shadow cache objects and offsets in the objects where the BPN is mapped. (Mtags)
Notes: Most common situation is when there is only one shadow cache object per guest paging object. But sometimes there can be many shadow caching objects for the same guest paging object.

## Slide 23: MMU data structures
MMUInfo Cache or Shadow Cache
  Shadow Cache Entry
Shadow Cache objects
  Shadow Roots
  Shadow Page Tables
MMU structure
Type of shadow cache object (page table / root),
bpn of the guest page table,
Link to the next shadow cache object for the same bpn.
MPN associated with the object, which contains the translated guest mappings etc.
MMUInfo Cache
Shadow Cache Entry 0
Shadow Cache Entry 1
Shadow Cache Entry 2
…
Shadow Cache Entry
Shadow Page Table / Root
mpn a + flags
mpn x + flags
mpn y + flags
…
Notes: MMUInfo is a list data structure that holds metadata of all the shadow cache objects. Each object in MMUInfo is identified by a ShadowCacheIndex or MMUInfoIndex. An entry of MMUInfo is called a shadow cache entry. MMU structure holds data regarding cached guest root, shadow root etc.

## Slide 24: Mtags, Backmap, Scratch AS
The mtags for bpns need to stored somewhere.
Until recently, stored in the busmem frame and spilled over into backmap, which lives in the Scratch AS.
Since busmem frames are VCPU shared, it bloats the size of the frame for very wide VMs. As a result the overhead memory of very wide VMs with large amount of RAM is pretty large.
Scratch AS is an address space created and used by the MMU to store all the mtags of guest bpns.
Monitor only. No address space constraints.
Still not cheap to use the scratch AS for every trace protection operation as getting in and out of scratch AS changes hardware CR3, which leads to hardware TLB getting flushed.

## Slide 25: MMU’s per-page overheads (<= vsphere 5.1)
Busmem Frame (2-vcpu VM)
MPN
Properties
Traces
Shadow list head idx
Mtag 0
Mtag 1 or Backmap pointer
Shadow list head idx
Mtags
vcpu0
vcpu1
Fixed or static part
Dynamic part
Notes: Fixed or static part of the busmem frame has a constant size irrespective of the number of VCPUs.

## Slide 26: MMU’s per-page overheads (<= vsphere 5.1)
Busmem frame size increases linearly with number of VCPUs.
Size of busmem frame can upwards of 788 bytes for a 64 vcpu VM.
Static overhead of a 4TB 64-vcpu VM would end up at 788GB or ~20% of VM memory size.
Notes: MMU is VCPU private. All other MMU overheads are dynamic and adjust based on demand. So we can do better.

## Slide 27: MMU’s per-page overheads
Step 1
  Move shadow list index head out of busmem frame.
  Managed in a new data structure called slHead, which is a open hash table.
  Size of slHead is dynamic and adjusts based on shadow cache size.
  Maximum possible size of slHead is 1MB based on the current maximum size of shadow cache.
  Always mapped in the monitor address space.
Notes: Busmem frames need to be zeroed at boot and during Vmotion when preparing destination. So having smaller busmem frames is desirable. At a point in time, guest pages that are page tables is a small subset of the total guest memory. Having slHead mapped in the monitor all the time saves a KSEG in BT64 and a potential cacheline pingpong for a multi-VCPU VM.

## Slide 28: MMU’s per-page overheads
Step 2
  Move mtags out of busmem frame.
  Managed in a two new data structures called mtagHash and mtagInfo.
  mtagHash is a open hash table and mtagInfo is a list data structure.
  mtagInfo contains bpn and mtag information on a per-page basis.
  mtagHash provides a powerful indirection layer so that mtagInfo can be managed as a cache without any constraints on placing the information in particular cache locations.
  Both mtagInfo and mtagHash are dynamically sized on demand.
  Mapped in the scratchAS for faster access in HV.
No MMU overhead in busmem frame any more.
Notes: Maximum possible overhead for a 64-vcpu 4TB VM is now ~20GB (shadow list head and fast mtag storing overheads).

## Slide 29: Dependent TLBs
CodeMap is an iTLB caches VRIP -> BPN mapping used by the decoder and translator.
VPHash is another iTLB, that caches VRIP -> TCA mapping. TCA is in-turn derived from a srcKey which has a BPN part among other things.
RTC (Return target cache), IC (inline caches) need to be kept in sync. IC is interesting as it needs to get updated only on global TLB flushes.
Monitor context of device code use MonTLB for fast access to traced memory. Caches LPN to BPN mappings and maps the MPN corresponding to the BPN at a different address in the monitor.
MonTLB needs to be kept in sync with shadows to avoid a “A-B-A” effect.

## Slide 30: Dependent TLBs (2)
DT, APIC, e1000 also use MMU to get notified when a LPN->BPN mapping changes. For example, when the pages of GDT/LDT are unmapped/remapped.
BT relies on MMU to provide a consistent LPN->BPN mapping even when doing back to back page walks during the period of a virtual instruction execution. S-TLB provides this consistent view for the BT subsystem.
MMU provides mapping change information to BT TLBs at a 2MB granularity called the range.
When MMU notices a mapping change, the dependent TLB which had expressed interest in the 2M region is notified. The dependent TLB could then get rid of the stale mappings.

## Slide 31: Difficult workloads for virtualized MMU
Workloads with a lot of MMU related activity such as
  Process creation (fork/wait)
  Context switches (Citrix)
  Page table updates

## Slide 32: HV with Software MMU
Use of hardware assist for instruction virtualization mostly removes the need for BT, however software MMU is still used.
Monitor and guest do not share the same address space.
VMCB/VMCS points to the shadow page table tree. Rest of the operation is similar to that of the MMU operation in BT mode.
Monitor lives in the Scratch AS all the time. Gives us plenty of address space when compared to 64MB when running with BT monitor. We can now map entire guest physical address space, busmem frames etc in the monitor all the time.
Exits are expensive, so hardware cost of #PF is pretty high. Try to avoid exits where possible.

## Slide 33: HV with hardware MMU
MMU virtualization support in hardware helps processor understand PPNs.
Hardware now walks another page tree to resolve the PPN to MPN.
Hypervisor is expected to maintain the tree providing correct PPN to MPN mapping.
So, with HWMMU,
  Guest page tables contain virtual to physical translation
  Second level tables contain physical to machine translation
  Using two tables, hardware converts virtual address to machine address
Shadow page tables are no longer necessary to virtualize guest page tables.

## Slide 34: HWMMU (2)
guest
CR3
LPN
MPN
TLB
TLB fill
hardware
nested
CR3
LPN -> PPN mapping
PPN -> MPN mapping

## Slide 35: Nested Page Walk
Happens on TLB miss
Guest structures (CR3, page tables) contain PPNs
  PPNs need to be converted to MPNs before memory access
  Full hypervisor tree walk for each level descended in guest tree
Upto 24 memory loads per TLB miss
  Compared to 4 in non nested case
  Increased TLB miss latency.
Hardware uses multiple levels of caching to avoid having to do 24 memory loads always.

## Slide 36: GPhys
Monitor implementation of the hardware walked second layer of page tables.
Contains mappings from PPN to MPN + flags.
Is the place to implement trace protection when running with hardware MMU virtualization assist.
Format of RVI NPTE is the same as a x86 PTE.
However, format of of EPTE is not.
GPhys handles this with multiple trees internally.
GPhys provides support for fast guest page walks used by HVSimulate for exit handling (mostly due to memory mapped I/O).
Supports platform large pages.

## Slide 37: Software MMU use with hardware MMU
Software MMU is still used when BT is required even when running with hardware MMU capable hardware.
Non-Paging mode cannot be handled by Nehalem processors.
BIOS, SMIs etc.
Smaller busmem frames.
Mtag-less zaps, but still targetted. We construct mtags dynamically.

## Slide 38: No latency on MMU intensive workloads
MMU related activity
  Process creation, context switches, page table updates
  BT monitor incurs huge overheads in these activities, HWMMU monitor incurs none.
No need to install traces on the guest page tables any more and scales better with number of VCPUs.
TLB miss rate
  TLB miss latency is significantly higher with HWMMU monitor (SPECJBB).
Use of large pages with hardware MMU (in Gphys) helps TLB intensive workloads tremendously when compared to that when running with software MMU.