## Slide 1: An In-Depth Look at Intel’s TLBs
Jim Mattson, Virtual Machine Monitor Team

## Slide 2
X86 page tables.
TLB details.
Paging structure caches.
Extended page tables.
Multiple address spaces.

## Slide 3: X86 Page Tables

## Slide 4: Long Mode Page Tables
PML4
PDPT
PD
PD
PDPT
PD
PT
PT
PD
PT
PT
PT
PT
PT
PT
LA 47:39
LA 38:30
LA 29:21
LA 20:12
Linear Address
Page Frame
Page Number
(LA 47:12)
CR3

## Slide 5: PAE Page Tables
PDPT
PD
PD
PT
PT
PT
PT
LA 31:30
LA 29:21
LA 20:12
Linear Address
Page Frame
Page Number
(LA 31:12)
MOV-CR3 preloads 4 PDPTEs

## Slide 6: 32-bit Page Tables
PD
PT
PT
LA 31:22
LA 21:12
Linear Address
Page Frame
Page Number
(LA 31:12)
CR3

## Slide 7: Other Paging Structure Contents
(P)resent Bit
Super Page (PS) Bit (in PD or PDPT entry)
Access Rights
  XD – eXecute Disable
  U/S – User/Supervisor
  R/W – Read/Write
Attributes
  (A)ccessed
  (D)irty (leaves only)
  (G)lobal (leaves only)
Memory Type
  PCD, PWT bits index into PAT MSR (non-leaves)
  PCD, PWT, PAT bits index into PAT MSR (non-leaves)
Reserved Bits

## Slide 8: Early Termination
A page walk will terminate early if:
A reserved bit is set (#PF).
The (P)resent bit is not set (#PF).
The super-page bit (PS) is set.
  PDPTE -> 1GB page [long mode only].
  PDE -> 2MB page [long mode, PAE] or 4MB page [32-bit].

## Slide 9: Cumulative Access Rights
PML4E
XD | U/S | R/W
PDPTE
XD | U/S | R/W
PDE
XD | U/S | R/W
PTE
XD | U/S | R/W
Translation
XD | U/S | R/W
|
&
&
&
&
&
&
|
|
#PF for rights violation(s) delivered only after completion of walk.

## Slide 10: A/D Bit Updates
(A)ccess bits are set before a paging-structure entry is used.
  If A=0, the MMU sets the A bit atomically with a second access.
(D)irty bit is set on leaf if access is a write.
  If D=0, the MMU sets the D bit atomically with a second access.
Validity is checked *before* write on second access.
  P=0 or reserved bit results in #PF.
Access rights are checked *after* write on second access.
  Could result in A=1, U/S=0 from a user-level read operation (#PF).
  Could result in D=1, R/W=0 from a write operation (#PF).

## Slide 11: Instruction Fetch Decoupling
Implicit page table accesses are not tracked as data dependencies.
Instruction fetch may race ahead of a previous store.
When storing to a paging structure, a serializing operation is necessary before a dependent instruction fetch.
None of the memory fence instructions are adequate.
Root cause of a few frobos bugs.

## Slide 12: TLB Details

## Slide 13: The TLB Abstraction
The TLB caches mappings from page number to:
  Page frame (physical address) and size.
  Access rights (XD, U/S, R/W).
  Attributes (dirty, memory type, global).
Only complete, valid translations are cached.
  Negative translations (those causing a #PF) are not cached.
The TLB is an incoherent cache.
  Changes to paging structures are not automatically reflected in the TLB.
  Software must ensure proper invalidation when modifying paging structures.

## Slide 14: Prefetching and Speculation
The TLB is updated as a result of speculative page walks.
  This includes speculative execution of data or uninitialized memory.
  Software must assume that any valid mapping in the page tables may be cached in the TLB.
  Root cause of some bugs in the vmkernel, the VMM, and frobos.
Speculative page walks never deliver a #PF.
  If a speculative page walk would have resulted in a #PF, no TLB entries are invalidated.

## Slide 15: Setting the (D)irty Bit
If a write access encounters a TLB entry with D=0:
The TLB entry is invalidated.
A new page walk is started from the root to set the (D)irty bit in the leaf.

## Slide 16: Access Rights Violation(s)
If an access violates the access rights recorded in the TLB,
  A #PF is delivered.
  The TLB entry is invalidated.
If the page tables have been modified to permit the access, the #PF may appear to be spurious.
AMD CPUs will not deliver such a “spurious” fault – an access rights violation in the TLB triggers a traversal of the page tables.

## Slide 17: Sandy Bridge TLBs
4K STLB (512)
4K ITLB (128*)
4K DTLB (64)
2M|4M DTLB (32)
1G DTLB (4)
2M|4M ITLB (7)
Super-pages may be fractured into multiple 4K TLB entries.
* 64 entries per thread with HT enabled.

## Slide 18: Haswell TLBs
4K/(2M|4M) STLB (1024)
4K ITLB (128*)
4K DTLB (64)
2M|4M DTLB (32)
1G DTLB (4)
2M|4M ITLB (7)
* 64 entries per thread with HT enabled.

## Slide 19: Multiple TLBs -> Conflicting TLB Entries
When changing the PS bit of a (P)resent paging structure entry:
  Clear the (P)resent bit.
  Invalidate all affected TLB entries.
  Write the new entry.
Failure to do so can result in multiple TLB entries for the same page number.
  The affects of this are undefined and implementation dependent.
Root cause of some frobos bugs.

## Slide 20: TLB Invalidation
#PF
  The TLB entry used to translate the linear address is invalidated.
A/D Bit Updates
  The TLB entry used to translate the linear address is invalidated.
INVLPG
  Any TLB entries associated with the page frame are invalidated.
MOV-CR0 (CR0.PG <- 0)
  All TLBs are flushed.
MOV-CR4 (PGE|PAE changes or CR4.PCIDE <- 0 || CR4.SMEP <- 1)
  All TLBs are flushed.
MOV-CR3 (CR4.PCIDE == 0 || CR3[bit 63] <- 0)
  All non-global TLB entries are invalidated.
Task Switch (CR3 changes)
    All non-global TLB entries are invalidated.

## Slide 21: Paging Structure Caches

## Slide 22: Paging Structure Caches
PML4
PDPT
PD
PD
PDPT
PD
PD
PML4E Cache*
PDPTE Cache
PDE Cache
LA 47:39
LA 47:30
LA 47:21 or 31:21 or 31:20
* PML4E$ is conceptual only.

## Slide 23: The Paging Structure Cache Abstraction
The paging structure caches cache mappings from page number prefix to:
  Page frame of next level in page table.
  Cumulative access rights (XD, U/S, R/W).
  Memory type for next level (from PCD/PWT).
Any valid partial walk may be cached.
  Full translations are not required.
  Root cause of some vmkernel and frobos bugs.
The paging structure caches are incoherent.
  Changes to paging structures are not automatically reflected in the caches.
  Software must ensure proper invalidation when modifying paging structures.

## Slide 24: Paging Structure Cache Invalidation
#PF
  Any entry used to translate the linear address is invalidated.
A/D Bit Updates
  All paging structure caches are flushed.
Various TLB invalidation instructions, including INVLPG
  All paging structure caches are flushed.
Task Switch (CR3 changes)
  All paging structure caches are flushed.

## Slide 25: Extended Page Tables

## Slide 26: Extended Page Tables (for all paging modes)
EPT PML4
EPT PDPT
EPT PD
EPT PD
EPT PDPT
EPT PD
EPT PT
EPT PT
EPT PD
EPT PT
EPT PT
EPT PT
EPT PT
EPT PT
EPT PT
gPA 47:39
gPA 38:30
gPA 29:21
gPA 20:12
Guest Physical Address
Page Frame
Page Number
(gPA 47:12)
EP4TA

## Slide 27: Guest-Physical Mappings
Derived solely from extended page tables.
Map guest physical page numbers (or prefixes) to page frames.
No TLB entries whatsoever for these mappings.
But there are guest-physical paging structure caches…

## Slide 28: Guest-Physical Paging Structure Caches
EPT PML4
EPT PDPT
EPT PD
EPT PD
EPT PDPT
EPT PD
EPT PD
EPT PML4E Cache*
EPT PDPTE Cache
EPT PDE Cache
gPA 47:39
gPA 47:30
gPA 47:21 or 31:21 or 31:20
* EPT PML4E$ is conceptual only.

## Slide 29: Guest-Physical Paging Structure Cache Invalidation
EPT Violation
  Any entry used to translate the guest-physical address is invalidated.
VM-Entry
  If the EP4TA is different from the EP4TA at the last VM-entry, these structures are flushed.
INVEPT instruction
  As directed.

## Slide 30: Combined Mappings
Derived from both guest page tables and extended page tables.
Map guest linear page numbers (or prefixes) to page frames.
Full translations occupy the “normal” TLBs.
Partial walks occupy the “normal” paging structure caches.

## Slide 31: Multiple Address Spaces

## Slide 32: Address Space Identification
An address space is identified by:
PCID – Bits 11:0 of CR3 when CR4.PCIDE is set.
VPID – Bits 15:0 of VMCS[VPID] when VPIDs are enabled.
EP4TA – Bits 51:12 of VMCS[EPTP] when EPT is enabled.

## Slide 33: ASID Table
Each thread maintains a 4-entry ASID table, which maps (PCID, VPID, EP4TA) to a 2-bit ASID.
ASID | PCID | VPID | EP4TA
0 | P0 | V0 | E0
1 | P1 | V1 | E1
2 | P2 | V2 | E2
3 | P3 | V3 | E3
On an ASID switch, the CPU looks up the new (PCID, VPID, EP4TA).
If a matching entry is found, it uses it.
If not, an entry is evicted, matching TLB and paging structure cache entries are invalidated, and the new (PCID, VPID, EPT4A) is installed in its place.

## Slide 34: ASID Tags
The STLB and L0 ITLBs are ASID-tagged.
  These can support multiple address spaces concurrently.
  They are not flushed on an ASID switch.
  The partitioning is dynamic.
The L0 DTLBs and paging structure caches are not ASID-tagged.
  These can support only one address space.
  They are flushed on an ASID switch.

## Slide 35: Tag-Based Invalidation
INVPCID instruction
  TLBs and paging structure caches are invalidated as directed.
INVVPID instruction
    TLBs and paging structure caches are invalidated as directed.
INVEPT instruction
  TLBs and paging structure caches are invalidated as directed (combined mappings).

## Slide 36: Hyperthreading
Only the 4K L0 ITLB is statically partitioned between the two threads on a core.
Other TLBs and paging structure caches are shared between the two threads on a core.
  Entries in these structures are tagged by thread ID.
  The partitioning is dynamic.

## Slide 37: Summary

## Slide 38: Key Takeaways
A/D bit updates may result in suspicious page table entries.
Instruction fetch may race ahead of page table updates.
TLB incoherence may result in one spurious fault.
Speculative accesses can populate the TLBs.
Multiple TLB entries may exist for the same page number.
Incomplete translations may be stored in the paging structure caches.
Only incomplete guest-physical mappings are cached.
Under EPT, combined mappings occupy the TLBs.
Some TLBs are ASID-tagged, where (PCID, VPID, EP4TA) -> ASID.
Some TLBs are dynamically partitioned by thread ID under HT.

## Slide 39: Questions?