## Slide 1: Frobos Memory Reliability Tests
Kelvin Fong

## Slide 2: Outline
Background
  PR 508941: Develop consistency check mechanism between VMM busmem and VMK pframe states
  Alex’s scenarios
Operations for the scenarios
  4 operations to implement
  How to implement the operations?
What a test looks like

## Slide 3: Background
PR 508941 Description – Ishan and Alex
PR 485914 shows an instance where an inconsistency between vmm's busmem frame and vmk's alloc pframes leads to data corruption. It would be nice to have a consistency check model to avoid or detect such cases in future.
*** Comment from Alex *** I think, though, that the question being asked is: is there a way to build a framework for the rmx vmkernel code that could allow it (and the monitor) to follow a script so that we could force certain kinds of interleavings and then build these up as a library of unit- and regression tests? An example of this for the monitor code is the frobos-based set of tests.

## Slide 4: Background
Update #12 – Alex’s scenarios
I think what we should do is choose a scenario that we'd like to script. Something like: * create a non-zero (hopefully unique) page * call into the vmkernel + get the page-scanning world to scan the page and install a hint + have the vmkernel request to swap this page out or like: * create a small page in a 2M region * call into the vmkernel + begin converting it to a backed-large page + immediately attempt to swap it out before the conversion completes or like: * create two identical pages of contents * call into the vmkernel + cause one of the pages to be pinned + handle p2mUpdate through the vmm to complete unsharing the page

## Slide 5: Operations for the scenarios
3 concurrent remapping scenarios, 4 operations to implement
  Share + swap same page
  Large page allocation/promotion + swap same page
  Share + pin same page
How to implement the operations?
  Should frobos call into vmm and vmkernel to script specific operations?
    This is easier, but may create bogus tests
  Or should frobos behave like a guest and invoke these operations like a guest?
    Sharing, large page allocations/promotions are still easy
    Swapping, pinning are less easy, but may still be possible

## Slide 6: Operations for the scenarios
Share a specific page
  monitor_control.disable_mmu_largepages=TRUE
  Frobos calls into vmkernel to set the page where scanning starts
VmMemCowPShareScanGetPage(const World_Handle *world, // IN
VmMemCow_State *cowState, // IN
Bool *fromQueue) // IN / OUT
{
...
pgNum = cowState->psharescanCurPage + 1;
if (UNLIKELY(pgNum == numMainMemPages)) {
pgNum = 0;
}
ASSERT(pgNum < numMainMemPages);
cowState->psharescanCurPage = pgNum;
return pgNum;
}
Large page mapping for a specific page
    HWMMU attempts large page allocation by default
      Disable sampling, no vMotion, FSR, large pages available, no swapping, …
    SWMMU (I haven’t done it yet, but I think it’s easy)
      Configure the guest mapping so gphys promotes the page large

## Slide 7: Operations for the scenarios
Pin a specific page
  Junyuan gets to figure this one out
  Currently looking at per-vm pinning in vmm via device buffer initialization
  Can also look at per-vcpu pinning in vmm, and vmkernel pinning
Swap a specific page
  (AFAICT) memsched triggers swapping for a world based on it’s memory state
    I’ve not been able to fake memory state to trigger swapping
    I think creating an actual low memory situation would prevent having sufficient control to trigger concurrent remapping scenarios (but I never tried it)
  Selecting a specific page remains a challenge
    Swapper selects pages randomly, then sequentially

## Slide 8: What a test looks like
for (i = 0; i < iters; i++) {
if (i > 0) {
pa[1] = MakePage(flags);
if (pa[1] == 0) {
break;
}
CopyPage((VA)pa[1], (VA)pa[0]);
}
SetPageOp(&op[0], pa[1], BUSMEMTEST_SETPSHARESCANCURPAGE);
SetEndCmd(&op[1]);
BackdoorCmd(cmdsPPN);
Timer_Sleep(1);
EXPECT_INT(memcmp(PA_TO_PTR(pa[0]), PA_TO_PTR(pa[1]), PAGE_SIZE), 0, "%u");
SetPageOp(&op[0], pa[1], BUSMEMTEST_TRYGETMPN);
SetPageOp(&op[1], pa[1], BUSMEMTEST_PFRAMEGETMPN);
SetEndCmd(&op[2]);
BackdoorCmd(cmdsPPN);
LOG(1, ("%u ppn=%#"FMT64"x vmm-mpn=%#"FMT64"x vmk-mpn=%#"FMT64"x\n",
i, PA_2_PPN(pa[1]), op[0].result, op[1].result));
if (i == 1) {
mpn = op[0].result;
EXPECT_TRUE(mpn != INVALID_MPN);
} else if (i != 0) {
EXPECT_INT64(op[0].result, op[1].result, "%#"FMT64"x");
EXPECT_INT64(op[0].result, mpn, "%#"FMT64"x");
}
}

## Slide 9: What a test looks like
typedef enum {
/* Test interfaces to BusMem calls. */
BUSMEMTEST_TRYGETMPN, /* BusMem_TryGetMPN() */
BUSMEMTEST_ISCOW, /* BusMem_IsCOW() */
BUSMEMTEST_ISMAPPED, /* BusMem_IsMapped() */
BUSMEMTEST_ISMAPPEDLARGE, /* BusMemIsMappedLarge() */
BUSMEMTEST_ISBACKEDLARGE, /* BusMemIsBackedLarge() */
...
/* Interfaces to Platform calls. */
BUSMEMTEST_PFRAMEGETMPN, /* PFrame_GetMPN() */
BUSMEMTEST_SETPSHARESCANCURPAGE, /* Set psharescanCurPage to bpn - 1. */
...
BUSMEMTEST_ENDCMD,
} BusMemTestOpType;
typedef struct {
PPN ppn;
BusMemTestOpType type : 16;
uint32 num : 16;
uint64 result;
} BusMemTestOp;
static void
TestMemory(void *unused)
{
uint32 flags = PTE_P | PTE_RW;
PA cmdsPa = MakePage(flags);
PPN cmdsPPN = PA_2_PPN(cmdsPa);
VA cmdsVa = cmdsPa;
BusMemTestOp *op = (BusMemTestOp *)(cmdsVa);