Host USB
Gengsheng Liu
CPD-Platform Team

---
Agenda
Agenda
The Introduction of USB
  - Basic Terms
  - USB Spec
  - Topology
  - Data flow
  - Descriptor
- VMware Virtual USB
  - Architecture
  - Device connect / disconnect
- Logging & Trouble Shooting
  - Logs
  - Tools

---
Basic Terms
Basic Terms
Host Controller （HC）
Hub & Root Hub
Port
Endpoint (EP0)
Pipe
Function
Device Address (Default Address 0)
Frame
Packet

---
USB Spec
USB Spec
USB 1.1 (UHCI, OHCI)
Low Speed (1.5MB/s), Full Speed (12Mbps)
USB 2.0 (EHCI)
Low Speed , Full Speed, High Speed (480Mbps)
USB 3.0 (xHCI)
Compatible with 2.0, Super Speed (5Gbps, 10bps)
USB OTG
Host
Device
Device
Device

---
Physical USB Topology
Physical USB Topology
PCI Bus

---
USB Data Flow Model
USB Data Flow Model

---
Windows USB Driver System
Windows USB Driver System

---
Data Flow Type
Data Flow Type
Control Transfers
Init & Configure USB device
Special data structure
Bulk Transfers
Large amounts of data, the data is sequential.
No latency requirement
Interrupt Transfers
Small data package， low latency
Isochronous Transfers
Isochronous data is continuous and real-time
bandwidth required
No ERROR Detection

---
Singe Packet Transfer
Singe Packet Transfer
Packet

---
Multi-Packet Transfer
Multi-Packet Transfer

---
Descriptor
Descriptor
Definition
A descriptor is a data structure with a defined format.
USB devices report their attributes using descriptors.
Descriptor Type
Device Descriptor
Describe general information about a USB device.
Length, Class, subclass, vender ID, product ID, Number of Configurations
Configuration Descriptor
Describe information about a specific device configuration.
Length, Config characteristics (Self-Power, Remote Wakeup), MaxPower, Number of Interface

---
Descriptor
Descriptor
Descriptor Type (Continue)
Interface Descriptor
Describe a specific interface within a configuration
Length, Interface Class & Subclass, Number of Endpoint
Endpoint Descriptor
Length, Transfer Type (Control, Isochronous , Interrupt, Bulk), Endpoint Address, Max Packet Size

---
Descriptor Relationship
Descriptor Relationship
Device Descriptor
Only one == >
Only One active configuration, determined at device init
Configuration 1
Configuration 0
Interface 0
Interface 1
Interface 2
Driver object
EP2
EP4
EP5
EP1
EP3
EP0 belongs to every Interface

---
Device State Diagram
Device State Diagram

---
VMware USB Architecture
VMware USB Architecture

---
Logs
Logs
vmware.log
VUSB Poweron, Init, USBIO, Device connect & disconnect
Arbitrator log
Record the connection / disconnection between VM and Devices
Hcmon log
Dynamic driver substitute
Filter & Change special Control Message
Hostd log
Record the USB device change event.
https://wiki.eng.vmware.com/USBBugGuidelines

---
Tools
Tools
lsusb
-t: Dump the physical USB device hierarchy as a tree
-v: show USB device’s descriptors
Usbview.exe
The same as lsusb, but on Windows
Virtual USB Analyzer
http://vusb-analyzer.sourceforge.net/tutorial.html
USB wireshark
http://esec-lab.sogeti.com/post/2011/04/06/Sniffing-USB-traffic-with-VMWare

---
Q & A
Thanks